## Slide 1
WHAT WE DID
We built a speech-to-speech translator on Param-2.
Shrutam-2 → Param-2 → Sooktam-2
Speak one Indian language — hear it spoken back in another. Three models chained end to end, deployed on a single H100.
CAPTURE
ffmpeg
browser mic → 16 kHz wav
→
TRANSCRIBE · ASR
Shrutam-2
speech → text
→
TRANSLATE · LLM
Param-2
text → text, target language
→
SYNTHESIZE · TTS
Sooktam-2
text → spoken voice
12 LANGUAGES
Indic, any-to-any
Hindi, Tamil, Telugu, Marathi, Bengali, Kannada & more.
LIVE WEB APP
Record in the browser
Get the transcript, the translation, and the spoken reply back — with per-stage timing.
ONE COMMAND
pod_setup.sh
Brings up all three models on the H100; ~30s warm restart after the first boot.

## Slide 2
WHAT WE SAW
Translation is the bottleneck — it's the model, not the pipeline.
Shrutam-2 → Param-2 → Sooktam-2
Where the ~10-second round trip goes — 24 profiled runs on one H100.
Translate
Param-2
6.9s · 67%
Synthesize
Sooktam-2
2.7s · 27%
Transcribe
Shrutam-2
0.6s · 5%
Capture
ffmpeg
0.1s · 1%
The tail is the real risk: the round trip is ~10s at the median, but p90 ~27s — and a ~60s cold start.
It's Param-2's variable “thinking,” not the rig: the service hop is 9 ms, and input length doesn't predict time (139 chars → 6.8s; 175 chars → 35s). ASR and TTS are already fast — the translator is the only lever.

## Slide 3
WHAT WE'RE ASKING
A lighter Param-2 for the translate step.
Shrutam-2 → Param-2 → Sooktam-2
Param-2 is a 17B “thinking” model — great for reasoning, heavyweight for a narrow translation. Would any of these be possible?
FOOTPRINT
A quantized Param-2
An INT8 / FP8 / 4-bit build — smaller on the GPU and faster to decode, so it fits beyond an 80 GB H100.
1
RIGHT-SIZED
A translation-specialized model
A smaller, distilled BharatGen model built for translation — instead of running a general 17B reasoning LLM for one MT step.
2
DECODE
A non-thinking / capped mode
Skip or cap the <think> budget for translation, where step-by-step reasoning isn't needed — directly cutting the variable slow tail.
3
Any of these keeps the pipeline 100% BharatGen models — while making it real-time and demo-ready.